## Slide 1: MPEG-DASH live-stream in an unstable environment
Instructors:
Itzik Ashkenazi, Aviel Glam (Rafael)
Team Members:
Avraham Ayaso, Lavy Raz

## Slide 2: Background

## Slide 3: MPEG-DASH

## Slide 4: Why over http?
Commonly used protocol
Uses standard port (port 80 or 443)
  Ensures the stream is rarely blocked by Firewall

## Slide 5: Mpeg-Dash livestreaming
The protocol main goal was to stream media files and wasn’t meant for live-streaming
Our research extends the protocol to achieve that with tolerable delay

## Slide 6: Goals
1. Implement algorithms that manage the buffer and adjust it to the changing bandwidth, while maintaining live streaming.

## Slide 7: Goals
2. Comprehensive analysis on each streaming session:
  algorithm’s specifications
  streaming statistics
  bandwidth utilization

## Slide 8
MPEG-DASH architecture
WebCam – Installed on top of the server pc. Generates the live video stream.
DashCast – Breaks the input stream into a sequences of small segments and stores them on the server.
Each segment is stored in several different bitrates.
It creates an MPD file which defines the available qualities, and more features of the segments stored on the server.
NodeJS – Exposes the MPD file and the sequences through Web interface. The client receives the segments data using HTTP GET commands.
WEB
netEM – Simulates an unstable network behavior on the client’s computer.
Capable of adjusting the BW, packet loss and bit error rate.
MPEG-DASH engine – Generates HTTP GET commands to the server asking for the best quality the client can stream while trying to maintain live stream.
Player Logic –
Plays the live video stream. 

## Slide 9: Our setup

## Slide 10
Our Research

## Slide 11: Work assumptions
There is only a single client
The results are based on simulations using NetEm to control BW
The camera is connected directly to the server

## Slide 12: Open sources

## Slide 13: WORK METHODOLOGY
Learn the protocol and the given tools
1
Discuss possible solutions to our problem
2
Implement our algorithms
3
Test and analyze our algorithms in different environments
4

## Slide 14: KPI - KEY PERFORMANCE INDICATOR
 - measures the theoretical utilization of our algorithms.
  The algorithm prediction vs. the actual download rate
MOTIVE:

## Slide 15: KPI – KEY PERFORMANCE INDICATOR
 = PREDICTED_DL_RATE/ACTUAL_DL_RATE

## Slide 16: KPI - KEY PERFORMANCE INDICATOR
 - measures the practical utilization of our algorithms:
  The requested BW vs. the optimal BW
MOTIVE:

## Slide 17: KPI – KEY PERFORMANCE INDICATOR
 = REQUESTED_BW / OPTIMAL_BW

## Slide 18: Implemented algorithms

## Slide 19: rate AdaptATION
Predicts based on last download rate
More prone to fail in live streaming.

## Slide 20: Buffer Regulation
Our priority is to maintain tolerable delay in live stream over quality.
We achieve that by regulating the client’s buffer, which holds the segments that are yet to be played.

## Slide 21: AIMD (Additive Increase Multiplicative Decrease)
Based on TCP protocol
Conservative algorithm

## Slide 22: MOVING MEDIAN
Based on statistics
Non-conservative algorithm

## Slide 23: Presentation

## Slide 24: results
PREF.ALG | MOVING-MEDIAN |  |  | AIMD |  |  | 
 | #segments=30 | #segments=20 | #segments=10 | =15 | =10 | =5 | Parameter Environment
MEDIAN (30) | 88.51 | 75.69 | 85.19 | 72.75 | 74.37 | 72.27 | Static
AIMD (15) | 75.46 | 83.82 | 80.06 | 94.81 | 91.42 | 74.93 | Quasi-static
MEDIAN (10) | 72.11 | 88.39 | 95.73 | 64.39 | 70.34 | 55.09 | Dynamic
MEDIAN (10) | 86.82 | 74.42 | 86.96 | 83.37 | 79.8 | 56.22 | Bursty
MEDIAN (30) | 82.3 | 71.48 | 62.49 | 65.05 | 71.48 | 42.82 | Noisy
 - theoretical utilization (%)

## Slide 25: results
PREF.ALG | MOVING-MEDIAN |  |  | AIMD |  |  | 
 | #segments=30 | #segments=20 | #segments=10 | =15 | =10 | =5 | Parameter Environment
MEDIAN (30) | 77.11 | 67.6 | 70.8 | 49.3 | 52.31 | 54.19 | Static
MEDIAN (10) | 65.21 | 64.74 | 67.52 | 62.08 | 61.63 | 50.61 | Quasi-static
MEDIAN (10) | 60.88 | 66.94 | 68.54 | 44.5 | 49.94 | 40.1 | Dynamic
AIMD (15) | 55.71 | 44.41 | 57.52 | 57.87 | 53.96 | 40.6 | Bursty
MEDIAN (30) | 45.44 | 42.48 | 33.47 | 39.12 | 42.9 | 25.66 | Noisy
 - practical utilization (%)

## Slide 26: Conclusions
According to our analysis:
The open source’s algorithms we tested didn’t fit for live-stream purposes.
  Due to improper regulation on the client’s buffer.
Moving-Median adapts to the client’s network better.
  Due to learning the network’s BW via the download rate history.

## Slide 27: Products and contributes
Accomplishing the goals of the project
Built a repository and instructions how to use it
Built a friendly infrastructure and GUI
Built and adapted new algorithms

## Slide 28: What we learned
MPEG-DASH protocol and different algorithms
Work with open sources and GIT
Explore and Analyze results

## Slide 29: Future ideas
Implement a learning method according to the client’s network
Improve the research to be more scalable

## Slide 30: Questions?

## Slide 31: Thank you